## Slide 1: A deconstructed comparison of DWM and LES wake aerodynamics
Joey Ray Bink &
Ignacio Héctor Caviglia
Report 19.10.2026

## Slide 2: Motivation
The IEC standard 61400-1 Ed. 4 recommends two models for the wake added turbulence: Sten Frandsen (SF) and Dynamic Wake Meandering (DWM)
General scientific agreement that SF overpredicts and DWM underpredicts damage equivalent loads (DEL):
Source | SF | DWM
Steiner, et al. (2025) [1] | - | Twr bot DEL 75% lower than LES + HAWC2
Bernard, et al. (2024) [2] | Twr top DEL 28% higher than measurements | Twr top DEL 35% lower than measurements
Reinwardt, et al. (2021) [3] | DEL 10-40% higher than measurements | DEL 2-10% higher than measurements
Larsen, et al. (2017) [4] | - | Twr DEL 20% lower than measurements
Andersen, et al. (2016) [5] | Effective TI 20-30% higher than LES | -
Larsen, et al. (2013) [6] | - | Twr DEL 15-20% lower than measurements

## Slide 3: Motivation
Mann model
+ SF
Mann model
+ DWM
LES

## Slide 4: Motivation
Central assumption of DWM: the transport of the wake deficit can be described as a passive-tracer driven by large-scale turbulence
This implies that there exists a moving frame of reference, where the wake deficit is independent of the large-scale motions
We will attempt to ”unsmear” the effects of wake meandering from an LES flow, to test whether meandering can be treated as independent from wake evolution
Source: T.J. Larsen et al., 2012

## Slide 5: Set-up
LES simulation results available (same as in Steiner et al., 2025):
  Single WTG (IEA 22MW): modeled as an actuator disc coupled to HAWC2
  Conventionally neutral boundary layer
  Resolution of 32 cells per diameter
  Wind speed planes (Y-Z) at 5D and 10D downstream the WTG, also 2D upstream

## Slide 6: Flow visualization

## Slide 7: Methodology: “Unsmear” workflow

## Slide 8: Methodology: Comparison against LES

## Slide 9: Expected outcomes
Test the validity of the “passive tracer” assumption
If the load results (HAWC2) using directly the LES flow vs the “re-constructed” flow match -> the passive-tracer hypothesis is an acceptable assumption for load estimations
If not -> this could explain the lack of accuracy of loads obtained using DWM
Other testing methodologies are also being discussed

## Slide 10: References
Larsen, T. J., Madsen, H. A., Larsen, G. C., & Hansen, K. S. (2013). Validation of the dynamic wake meander model for loads and power production in the Egmond aan Zee wind farm. Wind Energy, 16(4), 605–624. https://doi.org/10.1002/we.1563
Steiner, J., Hodgson, E. L., van der Laan, M. P., Alcayaga, L., Pedersen, M., Andersen, S. J., Larsen, G., & Réthoré, P.-E. (2025). A multi-fidelity model benchmark for wake steering of a large turbine in a neutral ABL. https://doi.org/10.5194/wes-2025-200

## Slide 11: A deconstructed comparison of DWM and LES wake aerodynamics
Joey Ray Bink & Ignacio Hector Caviglia
Report 26.10.2026